SUBWORKING GROUP:	Network

TASK:	TI TIF4

FILE NAME:	NTCO xxx

TITLE:	Interworking VoIP and Circuit-Switched Networks: the Gateway as a PSTN Switch

ISSUES ADDRESSED:	This contribution describes the VoIP PSTN access model as portrayed in the MGCP specification, concluding that the gateway is a PSTN switch.

SOURCE:	AT&T Canada (MetroNet Communications)

George W Turner

DISTRIBUTION:	Interested Parties

NOTICE:	This contribution has been prepared by AT&T Canada (MetroNet Communications) to assist the Canadian Industry, Network Working Group, as a basis for discussion.  This should not be construed as a binding proposal on AT&T Canada (MetroNet Communications).  Specifically, AT&T Canada (MetroNet Communications) reserves the right to add to, amend, or withdraw the contents of this contribution.

________________________________________________________________________

DATE:	January 13, 2000

Background and Purpose

At the 1999, 12, 07 Network Working Group meeting, ÒconcernsÓ were raised about the impact of interconnection between conventional circuit-switched networks and those using Voice over IP (VoIP) technology.  Specifically, there appeared to be alarm over the fact that the IP characteristics are not apparent to the conventional voice networks, and that consequently some unforeseen and extremely subtle impacts might occur.  These concerns appear to have been fostered by the characterization of the gateway as a protocol converter.

Examples of these concerns may be found in NTCO049 by Bell Canada and NTCO059 by Telus.

This paper is written as a Technical Interface Contribution, for the purpose of addressing some of the concerns raised in the aforementioned documents.  It is based on an interpretation of the current MGCP and SIP specifications, and represents one way of providing VoIP services.  The intent of this paper is to demonstrate that the gateway is specified to appear to the conventional circuit-switched networks as just another switch.  As such, it should be expected to pass a set of Industry conformance tests intended to confirm compatibility with existing circuit-switched standards, as adopted by the NTWG.

Discussion

Basic VoIP Access

Description

VoIP can provide end-to-end IP voice connectivity for telephony applications.  This may eventually lead to a requirement for IP interworking in Ònative modeÓ.  However, the current priority within the Canadian Industry, and the focus of this paper, is the use of VoIP between IP endpoints (i.e., phones or their equivalent) and gateways to the conventional circuit-switched world.  The prime objectives for VoIP access are straightforward and simple Ñ 1)Êto reduce the cost of the endpoints so they are suitable for deployment in residences and small businesses; and 2)Êto gain transport efficiency of voice over the copper loop, or other physical facility.  A powerful fringe benefit of the technology is a greatly enhanced service creation capability.

The gateway performs many functions, several of which have no relationship to telephony.  The part that is of interest is that which interworks the IP endpoints with the PSTN, entirely under the control of a Òcall agentÓ.  The MGCP describes the control interface between said call agent and the gateway in copious detail, because this is intended to be an open interface.  From a reading of this specification, it is clear that the functionality being described is that of a conventional digital switch.  Thus, the gateway should be viewed as a conventional switching matrix rather than a protocol converter, although protocol conversion certainly occurs in the process (as it does in any digital switch).

The VoIP network topology is portrayed as a triangle with embedded client endpoint, gateway, and call agent at the three points.  The MGCP forms the side between the gateway and the call agent, and allows the latter to control all the activities of the gateway point.  An RTP (Real Time Protocol for packetizing voice) forms the side between the endpoint and the gateway, and Session Initiation Protocol (SIP) is used between the endpoint and the call agent, as required.  From a physical standpoint, the call agent can be stand-alone, co-located with the gateway, or co-located with a group of endpoints.

Endpoints are simply terminations on the aforementioned switching matrix.  These terminations may be either physical or virtual Ñ for example, a phone connection on the one hand, or access to a time slot within the circuit-switched network on the other.  The gateway provides connections amongst two or more terminations under the direction of a call agent.  It is equipped with traditional utilities that allow it to perform this function, such as various event detection mechanisms, signal generators, and memory to store instructions from the call agent.

The MGCP specifies a set of primitives to enable the essential functions.  The following example illustrates how the scheme works in the handling of a typical call.

Acting on previously downloaded instructions from the call agent, the gateway detects a request for service from an endpoint.  The gateway accumulates signalling data from the endpoint, as it was requested to do in instructions sent previously by the call agent.  After a pre-defined trigger has been activated, the gateway sends a notification to the call agent, together with the collected data.  The call agent analyzes the data, determines a course of action, and then sends a command back to the gateway.  Typically, this command would be a request to set up a connection.  Subsequently, assuming a successful call has been concluded, the gateway detects a call termination event and sends an appropriate notification to the call agent, complete with statistical data about the call for use in billing, station message detail, or network administration.  As its final act in this example, the call agent instructs the gateway to delete the connection.

Observations

Although Internet Protocols are used on all three sides of the VoIP triangle, the protocol ceases to exist upon entry into any one of the three points.  Thus, there is no through path from the IP protocol on one side of the gateway to the PSTN time slots on the other side.  In fact, the MGCP calls for the gateway to support a multiplicity of protocols on the IP side, as specified by the call agent at boot-up time.  The gateway normalizes the protocols on all its voice interfaces to a vendor-specific protocol for internal use in establishing connections (or associations), and this may even be a standard PSTN time slot.

Signalling from the endpoint to the gateway is rudimentary.  The gateway can be instructed to look for hook-switch status, DTMF tones, and the presence of fax or modem tones.  No other signals are possible at this time.  The gateway traps all such signals and sends them to the call agent Ñ never directly into the PSTN.

Signalling from a call agent to the gateway consists of primitives.  These are: notification request, notification, create connection, modify connection, delete connection, request audit.  Given such an arrangement, generation of SS7 messages is implicit.  For example, the Òcreate connectionÓ primitive leads to generation of an SS7 Initial Address Message if the callÕs destination is in the PSTN.

In order to perform its functions properly, the call agent maintains a status map of all the endpoints under its control.  Thus, if the transport medium is becoming overloaded due to excess packets, the option is available to deny new attempts rather than to allow progressive degradation of all existing connections.

Delivery of Caller ID to the IP customer is consistent with TR-NWT-001188, GR-30-CORE, and TR-NWT-000031.  The SS7 fields towards the PSTN are currently populated by the gateway.

IP stations have standard telephone numbers, which are assigned by the LEC.  The endpoints have IP addresses.  The call agent manages the translation between the two in the same way that a PSTN switchÕs CPU matches a Directory Number (DN) to a Line Equipment Number (LEN).

Subtending Switches

Description

The MGCP is not intended to support subtending switches.  The endpoints are expected to be phones, not trunks.  Consequently, a viable method of signalling between these types of endpoints and the gateway is non existent.   However, work is proceeding in this area nonetheless, particularly with respect to IP PBXs.  This is because PBX vendors see evolution towards MGCP compatibility as essential to the continued relevancy of their products.

The solution is to put the call agent in the subtending switch where it can communicate with the switchÕs CPU via a proprietary bus.  Then there is no further need for signalling within the RTP and almost all functions can be supported.  The missing functionality is significant Ñ direct interworking with SS7 via the equivalent of ISDN PRI signalling.

The above solution is intended for IP PBXs.  However, this method has potential for expansion to any remote switch.  All that is needed is emulation of the characteristics expected of an endpoint.  However, the need to maintain these characteristics makes the results predictable and consistent with the model provided by MGCP.

Observations

When a gateway is supporting subtending switches, the endpoints are equivalent to trunks.  Consistent with traditional telephony practice, the call agent is aware of the busy/idle status of all the endpoints it controls.  Thus, when all the endpoints (i.e., trunks) are in use, conventional blocking takes place.  This can be measured.

The transport facility supporting the endpoints being used as trunks should be engineered to support simultaneous use of all the endpoints.  The gateway provides packet-handling statistics at the end of each connection and these can be used to determine packet loss and average delay for engineering purposes.  These anomalies, when and if they occur, contribute to noise and distortion, not blocking.

IP designers see the gateway as an opaque wall that blocks access to capabilities previously available via ISDN PRI.  There will be ongoing pressure to liberalize access to certain SS7 parameters, notably CLID and CNAM.  However, this access should continue to be tightly controlled by the gateway, in its role as a PSTN switch.

IP Signalling

Description

As stated at the outset, this paper assumes that end-to-end signalling will use SIP.  (H.323 is also available for this purpose.)  This protocol is currently being favoured by ÒnetheadsÓ because of its ability to support Òperson locatorÓ services.  The SIP Universal Resource Locator (URL) is assumed to be based on a phone number, given that numeric user names are supported in the protocol and most phones will be restricted to the use of a keypad for some time to come.  Accordingly, the URL is of the Òuser and hostÓ form, <SIP:6132265029@metronet.ca>.  Being system-generated, this address will not seen by phone users.  A Domain Name Service (DNS) translates the domain name (Òmetronet.caÓ) into an IP address for routing to the appropriate host server.  This function is analogous to Global Title Translation (GTT) in the SS7 world.

The first step in setting up a call via SIP is to locate the user.  This may be handled directly by the local server.  Failing this, the local server may simultaneously broadcast requests to any number of remote servers and analyze their responses for success.  Once the user has been located, permission is obtained to set up the call, taking into consideration the busy/idle status of the called party and the latterÕs willingness to accept a call from this particular caller.  The goal is to reach near certainty that the subsequent call will be successful, both in terms of having the right parties available at the specified locations, and of having agreement from the parties to talk at this time.  The association (i.e., the call) is established only after this level of confidence has been reached. There is no need for traditional call management services in such a scenario.

Observations

In terms of supporting new types of services, end-to-end SIP can provide more functionality than SS7.  It has orders of magnitude more throughput.  It is much faster.  Its global title translation process is not encumbered by having a limited number of service identifiers.  Thus, there appears to be no need to interwork signalling between IP networks and SS7.

The primary function of the gateway is to set up calls between IP-based users and those served by traditional circuit-switched networks.  Therefore, there is no need to enrich the interface described under Basic VoIP Access, unless additional capabilities are made available to PSTN users.

When (and if) the circuit-switched network is used to provide an end-to-end voice path between IP-based users (either within the same VoIP service providerÕs network, or between two VoIP networks with appropriate business agreements in place), Caller ID is not needed.  Instead, a Business Group ID and a matching token are required, and these may be inserted into the Caller ID fields.

At some point, the proliferation of Òperson locatorÓ services is going to force interworking of IP networks in native mode.  (Otherwise, the largest IP network would have an inherent competitive advantage.)  Working within an existing protocol, the NTWG will have to agree on the method to be used to share the information.  There will also be a need to coordinate the assignment of IP addresses across the Industry.

Conclusions

The gateway is intended to be a point of demarcation between VoIP networks and conventional circuit-switched networks.  Various IP protocols enter on one side of the gateway, and are either converted to a vendor-specific protocol for transiting the integral matrix, or terminate within the gateway.  RTP exemplifies the former and MGCP the latter.  If an unrecognized message is encoded into the RTP, it will emerge in the PSTN as noise or tone in a particular circuit (assuming a connection is in place; otherwise nothing at all will emerge).  The suite of recognized messages is small, and consistent with traditional telephony practice for loops.  There is no connection whatsoever between the MGCP and the PSTN.  SS7 messages emerge from the gateway implicitly, because of certain orders received via the MGCP Ñ for example, Òcreate a connectionÓ.

It has been claimed that internet technology is not state conscious.  This is certainly true for routers, and may be true for end-to-end VoIP telephony.  However, it is not true in the VoIP PSTN access model defined by MGCP.  The call agent is intended to know the status of all endpoints at all times, and an audit capability is provided to ensure accuracy.  Thus, it is capable of monitoring the number of simultaneous conversations in a cross section and taking appropriate action.  Therefore, agreed upon performance monitoring of common facilities can be supported.

The functionality described in MGCP is that of a distributed switch.  The embedded endpoints are remote peripherals, the gateway is the matrix, and the call agent is the CPU.  It is not appropriate to characterize the matrix component of this switch as a protocol converter.  Accordingly, the gateway appears to the circuit-switched network as a fully compatible network switch and should be treated as such.  As stated at the outset, it should be expected to pass a set of Industry conformance tests intended to demonstrate compatibility with existing circuit-switched standards, as adopted by the NTWG.

References

ANSI: Signaling System No 7 (SS7) Ñ SCCP, T1.112-1992

IP Telephony @ Videotron, Jun, 1999, Videotron Communications Inc

Netheads versus Bellheads: research into Emerging Policy Issues in the Development of Internet Protocols, Nov 11, 1999, T. M. Denton Consultants, Ottawa

PacketCableª Network-Based Call Signaling Protocol Specification, Pkt-SP-EC-MGCP-101-990312, Mar 12, 1999, Cable Television Laboratories, Inc

SIP: Session Initiation Protocol, request for comments 2543, Mar, 1999, Handley et al